###### U. S. FOREST SERVICE

###### ROCKY MOUNTAIN REGION

ENGINE OPERATOR GUIDE

MAY - 2000

The Rocky Mountain Region Engine Operator Guide provides a ready reference on the following topics for the various chassis, cabs, and slip-on units that are utilized. Use this guide and the vehicle operators manual, which are to be kept in the engines cab at all times when on the road.

- Applicable Specifications

- Operating Tips

- Maintenance

- Equipment Standards

The Guide is also intended to be a training text for all crew members. You will not find answers to all questions in this guide. More detailed information can be found in the manuals, booklets, and leaflets, (when available), that come with various engine components, plus USDA Forest Service handbooks and guides.

Engines used by the Forest Service to deliver water during wildfire suppression efforts are called upon to operate on mountain roads and in off-road assignments along firelines. They are required to operate under rough conditions of abnormally high stresses and vibrations. Preventive maintenance is critical to safe operation.

# DRIVER QUALIFICATIONS AND RESPONSIBLITIES

Due to the variety of chassis used in Region 2, license requirements will vary. Consult your state and Federal motor vehicle operators guide.

- Vehicles 26,001 lbs. and above require a Commercial Drivers License (CDL).

All personnel who operate Government owned-or-leased motor vehicles must meet qualifications stated in FSM 7136. An OF-346 is required for specialized equipment.

To avoid accidents, modern-day traffic conditions necessitate that drivers be responsible mature and skillful. Good drivers are critical to safe operations. They attain the required attitude and skills through a training program that includes both classroom and on the road instructions. The goal of this instruction  should be to develop proper driving habits and attitudes, including learning to exercise good judgment and restraint. Important factors that govern skillful driving include:

- Attitude of the driver.

- Satisfactory completion of driver training and testing program.

- Limitations and conditions of the vehicle.

- Physical features and terrain of the roadway.

- Weather and lighting conditions.

- Attitudes, behavior, and reactions of drivers in nearby vehicles.

Despite all mechanical improvements and automatic safety advances, the driver is still the key to traffic safety. Drivers must keep in good physical condition, have sound driving skills, and maintain proper attitudes. The attributes of a good driver are directly related to attitude, skills, knowledge, judgment, habits, and physical and mental fitness.

## Attitude

A good attitude is possibly the most important requirement of a good driver. A drivers attitude is reflected in the mental regard for self, for others, for the vehicle, and for the surrounding conditions. A driver with a poor attitude usually has an excuse for any adverse occurrence: the other driver was at fault, the roadway was bad, the intersection was blind, etc.

Attitudes are learned , they are not inborn; therefore, they can be improved! Unfortunately, the driver who is a nice person until behind the wheel is not rare. There is always the danger that upon climbing in the “rig” and acquiring the authority of red lights, siren, and several tons of vehicle, the driver feels suddenly like a “big shot” with no need to consider courtesy or safety.

The big shot attitude, of course, is wrong and only leads to trouble. Recent tests indicate that self-styled “experts” usually have an attitude of indifference that tends to cloud judgment and often results in an accident. Bad driving attitudes include:

- “Big Headedness” (i.e., over confidence, pride in past record, and faith in experience)

- False Conception

- Impatience

### Big Headedness

There are drivers who take too much far granted and have serene confidence that the vehicle will perform to their will. They count on other people to do the right thing at all times and feel that red lights and a siren will provide an impenetrable barrier that will keep them from harm. Some get puffed up from about an accident record and forget how just a little inattention can make the “clean slate” meaningless if you believe that being a driver for a long time will see you through any trouble. A lot of experience, in and of itself, is not enough. It must be supplemented by continuing comprehensive training and self analysis of one’s attitude and capabilities.

### False Conceptions

To many of us rely on guesses, estimates, legends, and hearsay, instead of facts, when we are behind the wheel. When 100 drivers where quizzed, 90 of them where short by more than 40 ft. when estimating the stopping distances at a given speed (at 20 m.p.h., the average driver will travel 45 ft. before breaking to a stop; at 30 m.p.h., 78 ft.).

## Skill

Records show that some drivers of exceptional skill are repeatedly involved in accidents, while less adept drivers often have good safety records. Skill does not necessarily mean safe driving performance.

Skill is ability plus training. Good driving is skill plus a good attitude; poor driving results from a bad attitude, even if coupled with skill. The extent to which skill is applied  becomes more important, in the end, than how much skill is developed.

## Knowledge

Good knowledge of the total engine (chassis-cab plus pumper unit), its capabilities and limitations, including knowledge of response routes, hydrant or water tank locations, and applicable rules and regulations are essential to skillful driving.

Drivers not having this knowledge are apt to be distracted and confused to the extent that they become accident prone.

## Habits

Habits are learned and acquired through training and self discipline. Breaking ingrained habits has long been recognized as more difficult than learning new, acceptable ones. This has been observed to be true for Forest Service operators; the acquiring of good habits is of maximum importance in driver training.

## Fitness

### Physical

Any assigned driver, who is the least bit ill, fatigued, drowsy, or affected by medication, should refrain from driving and request a relief driver. Additionally, crew leaders have the responsibility to replace any driver who appears not to be physically fit.

As to specifics for the first shift of a project fire, a driver should not spend more than 12 hours on duty. Even during emergencies, 8 hours should be the maximum time per day a driver should spend behind the wheel. No driver should operate a vehicle unless at least 6 hours of sleep were obtained during the previous 24-hour period.

### Mental

Mental fitness is affected by, and affects, attitude and can change from day to day, hour to hour, and minute to minute. Drivers must concentrate on driving, removing from their mind all distracting thoughts. If a driver does not have clear mind because of domestic problems, financial difficulties, or on-the-job conflicts with fellow workers and/or supervisor, then driver status should be surrendered or taken away.

### Judgment

Your performance as a driver hinges on whether or not you posses good sound judgment. You will posses such judgment with proper attitude, good skills, adequate knowledge, right habits, and suitable fitness.

## ENGINE OPERATION

## Preparing to drive

Adjust the driver’s seat so you can easily operate all controls. Check to see that there is nothing on the cab floor that might roll under the accelerator or the brake pedal once the vehicle is underway. Adjust all mirrors for maximum visibility to the rear. Fasten seat belts before starting the vehicle’s engine.  Familiarize yourself with gauges and controls.

## Driving

Start the vehicle in motion by using the lowest transmission gear speed that enables the engine to easily start the load without slipping the clutch. Accelerate smoothly and evenly to engine-rated speed.

When starting on a grade with the clutch engaged, the rpm will drop off significantly; when engine rpm falls off, do not disengage the clutch and try to increase the engine rpm. Doing so may damage the driveline components. After the initial drop in speed, the engine will recover and accelerate in a normal manner.

## Downhill Operation

Prevent overspeeding of the engine when going down long and steep grades. The governor has no control over engine speed when it is being pushed by the loaded vehicle. Operate in a gear that will permit an engine speed UNDER high governed rpm. Operating the engine beyond high governed speed will cause severe damage.

## Shutting Down of the Engine

Before shutting down the engines, operate at a low idle speed for 2 to 3 minutes to allow the hot areas in the engine and turbocharger to cool gradually and turbocharger to slow down. This shutdown procedure will extend the engine and turbocharger life.

#### Field Maintenance

Preventive Maintenance: The vehicle operator and crew leader are responsible for the performance of minor maintenance, lubrication and servicing of assigned vehicles and equipment at proper time of mileage intervals. Minor maintenance includes making simple adjustments to compensate for wear, tightening or replacing loose bolts or nuts and all similar tasks for which the operator is qualified and equipped.

Ensure that PM inspections are documented and routed through the appropriate fleet manager. Preventive maintenance tasks that should be performed on a regular basis include:

- Gear boxes for oil leaks			Brakes for proper operation

- Check when last serviced			Hydraulic brake system for leaks

- Engine drive belts for tightness		All lights and siren if equipped

- Nuts and bolts for tightness			All foot pedals

- Tires for proper pressure when cold		Mirrors for cleanliness

- Engine oil and coolant level			Spare tire inflation

- Batteries for water, corrosion, etc		Lug nuts for tightness

- Tires for wear and tear			Instruments and guages

Items that should be checked on a daily basis include:

- Engine Oil					Brake Fluid

- Power Steering				Inspect Fan and Drive Belts

- Check all lights				Pump oil (if applicable)

- Water level in tank				Coolant Level

- Prime Pump					Start and Run Pump

- Fuel Level					Windows for chips, cracks, etc

## Tire Inflation

Incorrect tire inflation pressures can have adverse effectrs on life and vehicle performance. Too low an air pressure causes increased tire flexing and heat build up. This weakens the tire and increases the chance of damage or failure and can result in abnormal tire wear, adverse vehicle handling, and reduced fuel economy. Too high an air pressure can result in abnormal wear, harsh ride, and increased chance of damage from road hazards. Check tire inflation pressures daily, including the spare tire. Always check these pressures when the tires are cold. Correct maximum cold inflation pressures are indicated on tire sidewalls.

## Torquing Wheel Lug Nuts

For both single and dual wheels, wheel lug nuts should be tightened alternately and evenly to the correct torque. Refer to manufacturers specifications. Never use oil or grease on wheel studs or nuts.  Always re-check lug nut tightness after driving a few miles if wheels have been removed.

## Power Steering

Maintain the power steering fluid level as noted in the vehicle operator’s manual using only the type fluid listed in the manual. Do not overfill. Also, check the tightness of the power steering drive belt. Replace the belt if it is deteriorated.

## Cooling System

When the vehicle engine is cold, check the level of the fluid in the radiator and also that in the surge tank, if any. There should be fluid to the radiator neck and to the level marked on the surge tank.  If not, add fluid as required.

WARNING: Do not remove  the radiator cap when the vehicle engine is hot.

Use only manufacturer recommended antifreeze in the cooling system and protect to –34 degrees (50/50 mixture). Check entire cooling system (radiator and hoses) for leaks or cracks; remove bugs and foreign material from the front of the radiator. Check the fan belt for approximately ¾ inch deflection between pulleys.  Replace the belt if it is cracked or deteriorated.

## Electrical System

Adjust the alternator drive belt for approximately ¾ inch deflection between pulleys. See that all electrical wiring is protected from moving parts and engine heat.

ENGINE SPECIFICATIONS for REGION 2

# Type 6 - MODEL 52 - 300 Gallon Capacity            Type 7 – 125 Gallon Slip-on Unit

#### VEHICLE/CHASSIS                                                                     VEHICLE/CHASSIS

Make:  Ford F-450 (Presently single source)                                    Make:  Ford F-350 (Single rear wheels)

### Passengers:  3 person bench seat                                                       Passengers:  3 person bench seat

### Drive:  Factory built 4x4                                                                    Drive:  Factory built 4x4

GVWR:  15,000 lbs.                                                                          GVWR:  9,900 lbs.

Front Axle – 6,000 lb. Dana 60                                                       Front Axle – 5,200 lb. Dana 50

Rear Axle – 11,000 lb. Dana 80                                                      Rear Axle – 6,830 lb. Dana 60

Ratios – 4:88 to 1                                                                             Ratios – 4:10 to 1

Engine: 7.3 liter (488 c.i.) 235 HP turbo diesel                               Engine: 7.3 liter (488 c.i.) 235 HP turbo diesel

Transmission:  ZF 6 speed HD manual                                           Transmission:  ZF 6 speed HD manual       w/overdrive                                                                                                                 w/overdrive

Brakes:  hydraulic front and rear disc w/antilock                  Brakes: hydraulic front and rear disc w/antilock

Tires:  LT 225/70R-19.5 all terrain tread                                       Tires:  LT 265/85R-16  E  all terrain tread

Fuel Tank:  36 gallon capacity                                                        Fuel Tank:  36 gallon capacity

Additional Options:  110 Amp Alternator                                    Additional Options: High output Alternator

Air Conditioning                                                                              Air Conditioning

AM/FM Stereo                                                                                 AM/FM Stereo

Cruise Control                                                                                  Cruise Control

Tilt Steering                                                                                      Tilt Steering

Trailer Tow Package                                                                         Trailer Tow Package

Skid Plate Protection                                                                         Skid Plate Protection

Daytime Running Lights                                                                   Daytime Running Lights

#### BODY REQUIREMENTS                                                             BODY REQUIREMENTS

Per Forest Service specifications including:                                             8 ft. Pickup Body

9 ft. 6 inches long and 8 ft. wide Stake Body

(9 ft. 3 inch length unacceptable due to size of M-52)

Crossmembers on maximum 16 inch centers

ENGINE WEIGHT SUMMARY SHEET

Engine Type:_____________   Engine Number:__________

### Vehicle Number:______________    Class:____________

### Unit:____________   Sub-Unit:_______________

Date:_____________               Date Vehicle Purchased_________________

Date Tank/Pumper Unit Purchased:______________

### Manufacturer’s Gross Vehicle Weight Rating (GVWR)    ________________

Manufacturer’s Front Axle Weight Rating (GAWR Front)________________

### Manufacturer’s Rear Axle Weight Rating (GAWR Rear)  ________________

##### ACTUAL WEIGHTS FULLY LOADED FOR FIRE

(Weigh each axle separately)

Front Axle:____________     Rear Axle:_______________

Total Weight:__________________

Comments:______________________________________________________________

________________________________________________________________________

________________________________________________________________________

Region 2 is implementing the following standard engine and operational procedures to ensure consistency and safety of equipment and personnel.  It is the region’s intent to establish minimum standards in order to meet manufacturer’s ratings, State and Federal Laws, and Forest Service policy in order to ensure the safety of employees by developing a guide to assist in defining the correct size vehicle for the size of engine/slip-on unit being considered.

## REGIONAL MINIMUM GROSS VEHICLE WEIGHT RATING (GVWR)

## FOR WATER CAPACITY

### 125 gal. Type 7 slip-on unit              Standard pickup or utility body              9,900 lbs. GVWR

300 gal. Type 6 Model 52 slip-on     9 1/2 x 8 ft. flatbed or 9 ft. utility         15,000 lbs. GVWR

750 gal. Type 5 Model 52 slip-on     12 ½ x 8 ft. flatbed                                26,000 lbs. GVWR

1,000 gal. Type 5 Model 52 slip-on   15 x 8 ft. flatbed                                   28,000 lbs. GVWR

**Note: 12,000 lb. GVWR trucks for 200 gal. Model 52 units are no longer acceptable.

Gross vehicle weight rating (GVWR) and gross axle weight rating (GAWR), both front and rear, is established by manufacturers.  Total vehicle GVWR and separate front and rear GAWR will be displayed either on driver’s door jam or panel behind the seat.

Each vehicle being used for firefighting shall be weighed at a certified scale.  Vehicle is to be fully loaded and fire ready including passengers, gear, fuel, water, and fire equipment.  Weigh each axle separately.  The front axle, rear axle, and total weight is to be documented using an Engine Weight Summary sheet which is enclosed.

FSH 7109.19 identifies a need to reduce vehicle loads by 10% as an off road use factor in order to minimize maintenance over the life cycle of the vehicle.  This rough road factor shall be incorporated when calculating the cargo load for an engine.  If actual weights exceed this factor engine shall be downloaded and a new engine inventory listing of fire equipment, personnel, and water weighed again and recorded.  Fire equipment inventory list and engine weight documents are to be kept with engine at all times and a copy to sent to Forest FMO.  Any changes in configuration of the vehicle or equipment will require additional weighing and updating of documents.

Weight and size, changing handling characteristics hauling large volumes of water, and off road/side hill operation of fire engines classifies Model 52 engines a very specialized piece of equipment.  Any driver of Model 52 fire engines is required to take a written and operational test by the Forest Driver examiner.  Document this on an OF-346 Driver’s Identification Card.

Visibility enhancement during hazardous situations such as smoke filled roads and cautioning other traffic that an emergency vehicle is in the area is very important.  The primary reason for any lighting devices being installed on fire engines is to enhance visibility in these situations.  Options such as flashing amber or white strobe lights for visibility are recommended.  The Forest Supervisor shall determine the need for installation of emergency red lights and siren on fire engines.  Installation of red lights or siren will classify the engine as an emergency vehicle and Forest Service specialized equipment requiring testing.  If determination to use such devices has been made, all drivers shall be trained in proper use, pass a written test by Forest Driver Examiner, and document it on an OF-346 Driver’s Identification Card.

Following is the Regional Standard Minimum Fire Equipment inventory list for type 6 and type 7 engines.  Additional equipment may be added provided the axle weight and total vehicle weight ratings (including the 10% rough road factor) are not exceeded.

TYPE 6/7 INVENTORY SHEET

|  | NFES | QTY | REMARKS | Item Weight | Total Weight 7/6 |
| --- | --- | --- | --- | --- | --- |
| Hand Tools |  |  |  |  |  |
| McLeod | 0296 | 1 |  | 5lb 14oz | 5lb 14oz |
| Pulaski | 0146 | *2 | * 1 on Type 7 | 5lb 14oz | 5lb 14oz, 11lb 12oz |
| Combi Tool | 0346 | *2 | * 1 on Type 7 | 3lb | 3lb, 6lb |
| Shovel | 0171 | 1 |  | 5lb 10oz | 5lb 10oz |
| Backpack Pump | 1149 | *3 | * 2 on Type 7 | 4lb 5oz | 8lb 10oz, 12lb 15oz |
| Fusees(case) | 0105 | *1 | * 1/2 case on Type7 | 36lb | 18lb, 36lb |
| Wetting Agent (qt) | 1316 | 2 |  | 5lb | 10lb |
| Foam (5-gallon) | 1145 | 1 |  | 46lb | 46lb |
| Chainsaw |  | 1 | SN# Model stihl 044 | 20lb 2oz | 20lb 2oz |
| Chainsaw Chain |  | 1 |  | 14oz | 14oz |
| Chainsaw Tool Kit | 0342 | 1 |  | 2lb 7oz | 2lb 7oz |
| Gas/oil Dolmar |  | 1 |  | 2lb 5oz | 2lb 5oz |
| Falling axe, 5 lb. |  | 1 |  | 5lb | 5lb |
| Drip Torch | 0241 | *2 | * 1 on Type 7 w/ fuel | 15lb | 15lb, 30lb |
| Portable Pump |  | *1 | * Optional on Type 7 | 9lb 10oz | 9lb 10oz |
| Medical |  |  |  |  |  |
| First Aid Kit(10 person) | 0068 | 1 |  | 2lb 12oz | 2lb 12oz |
| Body Fluid Barrier Kit | 640 | 1 |  | 2oz | 2oz |
| Hose |  |  |  |  |  |
| Booster ft/reel | 1220 | 200 |  | 100lb | 100lb |
| Suction 1 1/2" x 8' * | 0914 | 2 | * 2" on Model 52 | 7lb 4oz | 7lb 4oz, 14lb 8oz |
| 3/4" x 50' mopup (feet) | 1016 | *20 | * 10 on Type 7 | 28lb | 14lb,28lb |
| 1" x 100' | 1238 | *3 | * 2 on Type 7 | 8lb 8oz | 17lb,25lb 8oz |
| Mopup Wands | 0720 | 2 |  | 2lb 4oz | 4lb 8oz |
| 1 1/2" x 100" | 1239 | *3 | * 2 on Type 7 | 12lb 8oz | 25lb, 37lb 8oz |
| Nozzle |  |  |  |  |  |
| Forester 1"NPSH | 0024 | 2 |  | 2lb 5oz | 4lb 10oz |
| 1" adjustable NPSH | 0138 | 2 |  | 8oz | 1lb |
| 1 1/2" adjustable NH | 0137 | 2 |  | 9oz | 1lb 2oz |
| 3/4" adjustable NH | 0136 | 2 |  | 8oz | 1lb |
| Foam, 3/4" | 0627 | 1 | blizzard wizard | 2lb | 2lb |
| Foam, 1 1/2" | 0628 | 1 | blizzard wizard | 2lb | 2lb |
| Tip, Forester nozzle, fog | 0635 | 1 |  | 10oz | 10oz |
| Tip, Forester, straight stream | 0638 | 1 |  | 5oz | 5oz |
| Tip, Applicator | 0735 | 2 |  | 3oz | 6oz |
| Wye |  |  |  |  |  |
| 3/4" gated wye | 0739 | *6 | * 3 on Type 7 | 1lb | 3lb, 6lb |
| 1" gated wye | 0259 | 1 |  | 2lb 8oz | 2lb 8oz |
| 1 1/2" gated wye | 0231 | *2 | * 1 on Type 7 | 4lb 8oz | 4lb 8oz,9lb |
| Increaser |  |  |  |  |  |
| 3/4" NH-F to 1" NPSH-M | 2235 | 1 |  | 4oz | 4oz |
| 1" NPSH-F to 1 1/2" NH-M | 0416 | 1 |  | 5oz | 5oz |
| Coupling |  |  |  |  |  |
| 1 1/2" Double Female | 0857 | 1 |  | 9oz | 9oz |
| 1 1/2" Double Male | 0856 | 1 |  | 5oz | 5oz |
| Reducer |  |  |  |  |  |
| 1" NH-F to 3/4" NH-M | 0733 | *6 | * 3 on Type 7 | 3oz | 9oz, 1lb 2oz |
| 1 1/2" NH-F to 1" NPSH-M | 0010 | *4 | * 2 on Type 7 | 9oz | 1lb 2oz, 2lb 4oz |
| Tee |  |  |  |  |  |
| 1" NPSH x 1" NPSH x 1" NPSH | 2240 | 2 |  | 8oz | 1lb |
| 1 1/2" NH-F x 1 1/2" x 1" NPSH | 0230 | 2 |  | 1lb 2oz | 2lb 4oz |
| Valve |  |  |  |  |  |
| 3/4" NH Shut off | 0738 | 5 |  | 1lb | 1lb |
| 1" Shut off | 1201 | 1 |  | 1lb 1oz | 1oz 1oz |
| 1 1/2" Shut off | 1207 | 1 |  | 1lb 8oz | 1lb 8oz |
| 1 1/2" NH-F Automatic check bleeder | 0228 | *1 | * Optional on Type 7 | 2lb 10oz | 2lb 10oz |
| Foot Valve NH-F | 0212 | 1 |  | 2lb 3oz | 2lb 3oz |
| Wrenchs |  |  |  |  |  |
| Hydrant | 0255 | 1 |  | 6lb | 6lb |
| Spanner | 0234 | 2 |  | 5oz | 10oz |
| Pipe, 18" | 0934 | 1 |  | 5lb 14oz | 5lb 14oz |
| General Supplies |  |  |  |  |  |
| Collapsible pail | 0141 | 1 |  | 8oz | 8oz |
| Fire extiguisher | 2143 | 1 |  | 3lb 11oz | 3lb 11oz |
| Hose Clamp | 0046 | *2 | * 1 on Type 7 | 1lb 14oz | 1lb 14oz, 3lb 12oz |
| Flagging (rolls) |  | 5 |  | 6oz | 1lb 14oz |
| Batteries, AA | 0030 | 24 |  | 2oz | 3lb |
| Belt Weather Kit | 1050 | 1 |  | 2lb | 2lb |
| Fireline Handbook | 0065 | 1 |  | 12oz | 12oz |
| MRE | 1842 | 6 |  | 1lb 6oz | 8lb |
| Gas, Safety Can 5 gal. | 1291 | 1 | full | 47lb 4oz | 47lb 4oz |
| Canteen 4 qt | 1063 | 2 | full | 9lb 14oz | 9lb 14oz |
| PPE |  |  |  |  |  |
| Packsack | 0744 | 1 |  | 2lb 7oz | 2lb 7oz |
| Headlamp | 0713 | 1 | with 4AA batteries | 1lb 2oz | 1lb 2oz |
| Hard Hat | 0109 | 1 |  | 1lb 4oz | 1lb 4oz |
| Goggles | 1024 | 1 |  | 7oz | 7oz |
| Gloves | 1296 | 1 |  | 6oz | 6oz |
| Fire Shirt | 0580 | 1 |  | 1lb | 1lb |
| Fire Pants | 2021 | 1 |  | 1lb 4oz | 1lb 4oz |
| Chainsaw Chaps | 0150 | 1 | 36" | 2lb 9oz | 2lb 9oz |
| Ear plugs (pairs) | 1027 | 3 |  | .16oz | .5oz |
| Fire Shelter | 0169 | 1 |  | 3lb | 3lb |
| Equipment Belt | 1530 | 1 |  | 9oz | 9oz |
| TOTAL WEIGHT |  |  |  | 451lb 10oz | 510lb 3oz |

Engine #:

DAILY FIRE ENGINE INSPECTION CHECKLIST

| DATE |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
| MILEAGE |  |  |  |  |  |  |  |
| Cab/Chassis |  |  |  |  |  |  |  |
| 1. Oil |  |  |  |  |  |  |  |
| 2. Coolant |  |  |  |  |  |  |  |
| 3. Power steering |  |  |  |  |  |  |  |
| 4. Fan Belts |  |  |  |  |  |  |  |
| 5. Air cleaners |  |  |  |  |  |  |  |
| 6. Hoses |  |  |  |  |  |  |  |
| 7. Leaks |  |  |  |  |  |  |  |
| 8. Batteries |  |  |  |  |  |  |  |
| 9. Fuel Tank Full |  |  |  |  |  |  |  |
| 10. Hydraulic Fluid |  |  |  |  |  |  |  |
| 11. Slack Adjusters |  |  |  |  |  |  |  |
| 12. Parking Break |  |  |  |  |  |  |  |
| 13. Tires |  |  |  |  |  |  |  |
| 14. Hubs/Lug Nuts |  |  |  |  |  |  |  |
| 15. Undercarriage |  |  |  |  |  |  |  |
| 16. Cabinet Locks |  |  |  |  |  |  |  |
| 17. General Condition |  |  |  |  |  |  |  |
| 18. Start Engine |  |  |  |  |  |  |  |
| 19. Lights/ signals |  |  |  |  |  |  |  |
| 20. Mirrors / Glass |  |  |  |  |  |  |  |
| 21. Back up Alarm |  |  |  |  |  |  |  |
| Remarks: |  |  |  |  |  |  |  |

| 22. Gauges |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 23. 2 way radio |  |  |  |  |  |  |  |
| 24. Wipers Washers |  |  |  |  |  |  |  |
| 25. Horn |  |  |  |  |  |  |  |
| 26. Seat belts |  |  |  |  |  |  |  |
| 27. Heater AC |  |  |  |  |  |  |  |
| 28. Log Book |  |  |  |  |  |  |  |
| 29. Accident Forms |  |  |  |  |  |  |  |
| 30. Fire Extinguisher |  |  |  |  |  |  |  |
| 31. First Aid kit |  |  |  |  |  |  |  |
| 32. AIDS Kit |  |  |  |  |  |  |  |
| 33. Reflector Set |  |  |  |  |  |  |  |
| 34. Wheel Chocks |  |  |  |  |  |  |  |

| Pump Package |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 1. Water Tank Full |  |  |  |  |  |  |  |
| 2. Valves |  |  |  |  |  |  |  |
| 3. Oil Level |  |  |  |  |  |  |  |
| 4. Fuel Tank Full |  |  |  |  |  |  |  |
| 5. Air Cleaner |  |  |  |  |  |  |  |
| 6. Gauges |  |  |  |  |  |  |  |
| 7. Override Switch |  |  |  |  |  |  |  |
| 8. Live Reel |  |  |  |  |  |  |  |
| 9. Primer |  |  |  |  |  |  |  |
| 10. Foam System |  |  |  |  |  |  |  |
| 11. Foam Tank Full |  |  |  |  |  |  |  |
| 12. Water Level indicator |  |  |  |  |  |  |  |
| Remarks |  |  |  |  |  |  |  |

Engine #:

# Periodic/Post-Fire Inspection

## Cab/Chassis

| 1. Differential Oil Level |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 2. Transfer case Oil Level |  |  |  |  |  |  |  |
| 3. Check Drive Lines |  |  |  |  |  |  |  |
| 4. Parking Brake |  |  |  |  |  |  |  |
| 5. Manual Transmission Fluid |  |  |  |  |  |  |  |
| 6. Air Cleaners |  |  |  |  |  |  |  |

Pump Package

| 1. Check Service Log for Oil And Filter |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 2. Check Pump Motor Mounts |  |  |  |  |  |  |  |
| 3. Check Water Tank Mounts |  |  |  |  |  |  |  |
| 4. Check Spark Plugs |  |  |  |  |  |  |  |
| 5. Fuel Filter |  |  |  |  |  |  |  |
| 6. Clean / Change Air Filter |  |  |  |  |  |  |  |
| 7. General Appearance |  |  |  |  |  |  |  |
| 8. Pump Performance Test |  |  |  |  |  |  |  |
| 9. Lubricate Pump Head |  |  |  |  |  |  |  |
| 10. Foam System |  |  |  |  |  |  |  |
| Remarks |  |  |  |  |  |  |  |

Engine#:

# Pump Maintenance Log

| DATE | PUMP HOURS | OIL CHANGED | AIR FILTER | OPERATOR | REMARKS |
| --- | --- | --- | --- | --- | --- |

Winterization Checklist

Drain all pumps, valves, plumbing, foam unit, and water tank.  Blow out system with compressed air and add a small amount of antifreeze and water to low spots.

| Date: | Completed By: |
| --- | --- |

# Pump and Motor

| Oil Change |  | Wash Motor |  |
| --- | --- | --- | --- |
| Drain Pump |  | Change Air Filter |  |
| Grease Pump |  | Remove Strainer |  |
| Drain Plumbing |  | Open Valves |  |

# Foam System

| Flush System |  | Drain Selector Valve |  |
| --- | --- | --- | --- |
| Drain All Lines |  |  |  |

Hose Reel

| Drain Hose |  | Drain Reel |  |
| --- | --- | --- | --- |
| Remove Nozzles |  | Inspect & Grease Gaskets |  |

Tank

| Drain & Flush |  | Inspect tank and Baffles |  |
| --- | --- | --- | --- |

Engine

| Tighten All Bolts |  | Anti-Freeze Test –40 |  |
| --- | --- | --- | --- |
| Inspect All Lights |  | Fuel Filter |  |
| Break Fluid |  | Change Oil |  |
| Antifreeze in wiper fluid |  | Replace Air Filter |  |
| Clean Radiator |  | Inspect Fan Belts |  |
| Power Steering Fluid |  | 2 Way Radio Off |  |
| AM/FM Radio Off |  | AC/Heater Off |  |

Under Carriage

| Transfer Case Fluid |  | Front Differential Fluid |  |
| --- | --- | --- | --- |
| Rear Differential Fluid |  | Check and Note Any Leaks |  |
| Grease All Zerks |  | Inspect Tie Rods |  |
| Inspect Drive Lines |  | Inspect Springs and Hangers |  |
| Inspect Break Pods |  |  |  |
| Tire Condition (circle one) Poor Fair Good |  | Pump Package Mounting Brackets |  |

Boxes

| Hand Tools Clean, Sharp, & Painted |  | Clean Interior of Boxes |  |
| --- | --- | --- | --- |
| Clean Fuel cans & Drip Torches |  | Fire Extinguisher Serviced and Stored |  |
| Lock Boxes |  | Key In Office |  |

# Region 2 Engine Crew Performance Standard

Required standards

| 1 | Report to Dispatch | The firefighter will be able to give a complete and accurate initial report to the dispatcher or incident commander. |
| --- | --- | --- |
| 2 | Foam Generation | The engine operators will be able to produce foam from a nozzle within 15 seconds from time of charged hose. |
| 3 | Running Attack | To develop a crew’s team work in a running attack operation, the crew will be able to set up and perform a running attack. |
| 4 | Simple Hose Lay | To enable the crew to lay out 2 100 ft sections of hose in 2 minutes and 15 seconds. |
| 5 | Progressive Hose Lay | To enable the crew to lay out 3 100 ft sections of hose in 4 minutes and 30 seconds. |
| 6 | Pre-connected Hose | Crew will demonstrate use of pre-connected hose for IA of spot/remote fire and vehicle protection. |
| 7 | Broken Hose | When a broken hose occurs, the firefighter will be able to correctly shut off the flow with a hose clamp, replace the broken section, and recharge the line in 1 minute and 15 seconds. |
| 8 | Fitting Identification | The firefighter will be able to identify every fitting and explain uses of each item that is carried on the engine. |
| 9 | Valve Usage | The firefighter will be able to demonstrate the proper valve combination for the various situations given. |
| 10 | Drafting | The firefighter will be able to fill the engine’s water tank using the prescribed methods. |

Optional Standards:

| 1 | Get Away Time | The crew will be able to get away from the station within agency standards, insuring that the station is locked and PPE is on. |
| --- | --- | --- |
| 2 | Engine Equipment Location | To insure that the firefighter knows the location of all the engine’s equipment, the firefighter will find five given items without searching for them. |
| 3 | Foam Equipment Maintenance | The engine operator will be able to flush the foam system according to manufactures procedures |
| 4 | Line Construction | A five person crew will be able to construct 2.5 chains of line in 30 minutes. The drill will be done in local fuel and the line will be constructed in accordance with the fireline handbook as to proper width and depth. |

Optional Individual Requirements:

| 1 | LCES | Must be able to identify meaning of LCES and tell how it is applied. |
| --- | --- | --- |
| 2 | 10 Standard Fire Orders | Must be able to state the 10 Standard Fire orders |
| 3 | 18 Watch Out Situations | Must be able to state the 18 Watch Out Situations |
| 4 | Fire Shelter | Must be able to adequately prepare and deploy a fire shelter following all procedures |
| 5 | Line Location | Must be able to describe both direct and indirect line and when each is used. |
| 6 | Engine Placement | Must be able to demonstrate proper placement of engine given a specific situation. |
| 7 | Origin & Cause | Must be able to describe how to protect a fire origin and determine a preliminary cause. |
| 8 | Size Up | Must be able to give proper size up information and need for additional resources given a scenario. |

R-2 Engine Knowlege and

Skills Test

1.   (T or F)  Baffles are to control forward and backward surge.

2.   (T or F)  Engines should take curves, on-ramps and off-ramps at posted speeds.

3.   At the first sign of a problem with the  engine you should:

A.  Go to nearest service station to have a mechanic look at problem.

B.  Keep driving until there is no doubt there is a problem.

C.  Stop immediately and find the problem.

D.  Return to station.

4.   How do you test hydraulic brakes?

5.   You should inspect the engine:

A.  Daily

B.  Weekly

C.  Monthly

D.  At every stop

E.  All the above

6.   When backing why is it important to use a helper?

7.   What is the most important hand signal you and the helper should agree on?

A.  Left

B.  Right

C.  Stop

D.  Start

R-2 Engine Knowlege and

Skills Test (cont.)

8.   (T or F)  Reaction time and road surface condition equals stopping distance.

9.   When going down grades you should:

A.  Brake only when speed limit is achieved.

B.  Down shift before going down hill.

C.  Select appropriate gear (usually 1 lower that it takes to go up the same hill).

D.  B and C

10.  Gross Vehicle Weight Rating (GVWR) for every engine is:

A.  15,000 lbs.

B.  13,500 lbs.

C.  Specified on vehicle ID plate inside door or behind seat

D.  none of the above

11.  How do you know when to shift gears?

12. How much is rough road reduction factor?

13.  (T or F)  You should avoid side hilling on rough terrain.

14.  Chock blocks should be used:

A.  When parked on steep hills.

B.  When changing a tire.

C.  When parked on level ground.

D.  All the above

15.  If stopped on a hill how can you start moveing without rolling back?

16.  Name 3 Safety-Emergency equipement items that must be carried on the   engine.

1.

2.

3

R-2 Engine Knowlege and

Skills Test

ANSWERS

1.   True.  Baffles do control surge.  ref. common knowlege

2.   False.  Engines should take curves, on-ramps and off-ramps below posted speed.  ref. common  knowlege

3.   C.  ref. EM-7130-2

4.   Pump 3 times then hold for 5 seconds.  ref.5709.11

5.   E.  ref.6709.11 10-14, EM-7130-2

6.   The helper may be able to see what the driver cannot.  ref. common knowlege

7.   C  ref. common knowlege

8.   False.  Reaction time plus brake efficiency plus road conditions equal stopping

distance.   ref. EM-7130-2

9.   D  ref. 6709.11 10-15, EM-7130-2

10.  C

11.  When the RPM's get to a certian point as specified in the owners manual.

- Reduction of 10% of GVW.  ref. 7109.19

- True.  Having a higher center of gravity and water surge, engines are more likely to have problems side-hilling.  ref. common knowlege

14.  D  ref. 6709.11, EM-7130-2

15.  Partilly engage clutch before you take your right foot off of the break.  Parking break can also be used in this manner.  EM-7130-2

16.  Reflective triangles, fire extinguisher, first aid kit, extra fuses  ref. 6709.11

Operational Test

1.  Inspection

2.  Backing up to with-in 1.5 feet of mark.

3.  Pulling forward to with-in 1.5 feet of mark.

4.  Make right hand turn on corner, having rear tire come with-in 3 feet of corner with out     hitting corner.

5.  Safely change tire.

6.  Take off on steep hill with out rolling back.

7.  Down-shift and up-shift at the correct RPM's.

8.  Appropriatly shift to and from four wheel drive.

9.  Correctly select gear and brake when going down steep grades.

DRIVING HOURS  - Health and Safety Code Handbook 6709.11

12.3 - Safety Practices.  Vehicle operators shall comply with all traffic laws, regulations, or ordinances, even in emergency driving situations (sec. 12.32).

12.31 - Work/Rest Guidelines.  Vehicle operators must comply with these work/rest guidelines except for limited exceptions (during the first 24 hours) of emergency driving situations (sec. 12.32).

1.  Employees and contractors operating Government vehicles shall drive:

a.  Only if they have had at least 8 consecutive hours off duty before beginning a shift.

b.  No more than 2 hours without a rest stop.  Operators of vehicles carrying 16 or more passengers (including the driver) shall stop for 10 minutes every hour.

c.  No more than 10 hours per shift.  A shift must not exceed 16 hours, from beginning of shift to the end of shift including rest and meal stops.

2. Contractors operating Government commercial motor vehicles must adhere to   the hours of service for drivers as required by the U.S. Department of  Transportation (DOT) (sec. 12.01).  An exception may be made only when an emergency is officially declared.

12.32 - Emergency Driving.  Determine the type of emergency before driving.  Emergency situations shall be justified in writing and approved in writing by the appropriate line officer.

1.  When transporting passengers during an officially declared emergency, follow these precautions:

a.  National or State emergency.  Declared by the President or Governor.  Base allowable driving hours on the driving assignment, from starting point to destination.  Upon the driver's arrival at the destination, do not permit further driving if work/rest guidelines in section 12.31 have been exceeded.

b.  Regional emergency.  Local decision made by the line officer to provide direct assistance to supplement State and local efforts and capabilities to save lives.

2.  Where city or county ordinances require emergency vehicles using a siren and red lights to continue their route of travel regardless of traffic signals, drivers shall comply with such ordinances;  however, such travel through an intersection shall never exceed 10 mph (16 km/hour).