AVIATION INCIDENT/ACCIDENT

RESPONSE

GUIDE

Reviewed by:                            			         Date:

| Cathy Hutton | January 1999 |
| --- | --- |
| Cathy Hutton | March 2000 |
| Stacy Gray | May 2001 |
| Scott Howland | March 2002 |
| Pat Butler | February 2003 |
| Molly Campbell | April 2004 |
| Mark Howerton | March 2005 |
| Nick Janota | June 2006 |

AIRCRAFT ACCIDENT/INCIDENT GENERAL INFORMATION

It is important that you take a few minutes to become familiar with this guide.

This guide establishes the actions to take in the event of an aircraft incident, accident, or search and rescue.  The intent is for this guide to be reviewed and revised to fit the needs of the local user.  The scope of this guide outlines the basic procedures necessary to activate all emergency, crash, search, rescue, and associated support services as rapidly and orderly as possible.  Only after local updating will this guide satisfy the needs of a thorough plan of action.  It is recommended that this guide be updated annually.

This guide has four major categories:

- Missing Aircraft

- Overdue Aircraft

- Aircraft Accident - Aircraft Within Crash/Fire/Rescue Airport's Response Area.

- Aircraft Accident - Aircraft Away From Crash/Fire/Rescue Equipped Airport.

Each category lists priorities and actions to follow.

Additional information is provided in the appendices to assist in the planning and execution phases of Crash, Search, and Rescue.

PLAN * ACT * INFORM * COORDINATE * LOCATE * RECOVER * SECURE * RECORD

Someone's Life May Depend on Your Actions

SIX THOUGHTS

(Thoughts to consider in any aviation operation)

1.  You are now in charge of a sacred trust, the safety of human lives.

2.  You must not let undue pressure (expressed or implied) influence your judgment during the performance of your duties.

3.  You must be able to develop a team in which members must participate and contribute to the safety of the operation.

4.  You must delete the terms ``false pride,'' ``calculated risk,'' ``real world,'' and ``good enough for Government work''

from your professional vocabulary.

5.  You will not be criticized or stigmatized for any decision you make which will ensure added safety to an operation.

6.  You must not let your actions instill the attitude of competition between pilots.  This attitude may hinder their performance and may compromise the safety of the mission.

#### OVERDUE AIRCRAFT  OVERDUE AIRCRAFT

An aircraft normally will be initially considered ``overdue'' when it has not completed a required check-in by radio or     telephone within the time frame specified in the flight following request.  This time frame may be an elapsed period of time such as ``every 15 minutes'' for reconnaissance flights or may be Estimated Time of Arrival at a destination or reporting point.  Dispatchers or persons responsible for Flight Following are responsible for initiating actions and documenting all actions, contacts, conversations, and times, as specified by this guide.  Remember, it is also important to notify all parties of any changes in status including locating the aircraft.

If overdue aircraft is located at its destination or with only communications problems preventing contact, cancel   with all parties previously notified.  If the overdue aircraft is not located before anticipated, fuel exhaustion or (better yet)    at another time designated by the agency, declare the aircraft missing and proceed with the search and rescue (SAR) phase (see Missing Aircraft checklist).

| Action Initiated And Time | Date/Time Accomplished | Contact Action | Commercial Number | 24-Hour Number |
| --- | --- | --- | --- | --- |
| Immediately at overdue time |  | Attempt contact via radio (direct or relay) or through telephone calls. |  |  |
| 15 minutes or as designated by agency |  | Continue attempts within agency (originating/destination airport, agency/location, etc.). | Continue calling on the radio every 5 min. |  |

| 30 minutes or as designated by agency |  | Contact vendor base for possible communication with aircraft. | See Flight Request for aircraft info. |  |
| --- | --- | --- | --- | --- |

| After unsuccessful vendor contact, (at 30 minutes). |  | Call FAA Flight Service Station, (1-800-843-5619) giving flight information and request the specific action desired: communication check, ramp checks, or ELT reports (from SARSAT and/or known aircraft in area). SPECIFICALLY STATE THAT SEARCH AND RESCUE PROCEDURES ARE NOT REQUESTED AT THIS TIME. | Call local Airports to see if the aircraft has called in or if airport can reach them on 122.5 frequency. LOCAL AIRPORTS Meeker…….……………878-5045 Rangely………….……..675-2316 Hayden…………………276-5010 Emergency…………276-5034 Kremmling……….. 970-724-0611 Craig………….…………824-6335 Rifle……………..…970-625-1091 Grand Junction...…970-245-0652 Steamboat Springs..…..879-1204 Rangely after hours…...675-5179 |
| --- | --- | --- | --- |

| 1 hour or when known fuel duration is exceeded. |  | Notify local agency aviation manager or next level higher aviation manager to determine if missing aircraft procedures should be activated. | Cathy Hutton W(826-5032/5037) H(826-0694) |  |
| --- | --- | --- | --- | --- |

IF AIRCRAFT IS LOCATED AND HAS NOT EXPERIENCED A MISHAP

CANCEL ANY SEARCH/RESCUE PROCEDURES THAT HAVE BEEN INITIATED

AND COMPLETE SAFECOM

IF AIRCRAFT IS DETERMINED TO BE MISSING, GO TO MISSING AIRCRAFT SECTION

##### MISSING AIRCRAFT

An aircraft is officially missing when its fuel duration, as reported on its request for flight following or as reported on it's FAA Flight Plan, has been exceeded and the aircraft's location is not known.  Agencies have the option of instituting missing aircraft procedures at any time prior to fuel exhaustion time.

The Missing Aircraft designation requires that all the items on the following check list are completed and available for reference purposes when conducting this phase. Documentation of all actions, contacts, conversations, and time is an absolute necessity during the missing aircraft phase.

The Missing Aircraft phase cannot be conducted solely in-house by the agency.  The National Search and Rescue (SAR)   Plan requires coordination with SAR agencies.

Although one or two items in the sequence may be unknown at the time START THE ACTION.  Keep an accurate written log and fill in the blanks as best you can.

As much as possible obtain the following information on the missing aircraft:

CAUTION: Do not announce over the radio the names of individuals involved in missing aircraft.

1. Name of pilot(s):

2. Name of passenger(s). How many?

3. Aircraft registration number ``N'' -

4. Type of aircraft -

5. Color of aircraft -

6. Type of mission -

7. Last known location, time, latitude, and longitude.

8. Point of takeoff and time.

9. Destination and ETA.

10. Was flight plan filed with FAA or Agency?

MISSING AIRCRAFT

| DATE/TIME NOTIFIED | Action | Telephone |
| --- | --- | --- |

|  | The FAA Flight Service Station (FSS) is the entry agency into the National SAR system. Pass all missing aircraft data to the FSS. The FSS will notify the Air Force Rescue Coordination Center (AFRCC) who, in turn, will coordinate with the proper state (Aeronautics or Emergency Services) or County (Sheriff or Emergency Services) as appropriate under the National SAR Plan. | Grand Junction Control Tower: 970-243-3745 Denver ARTCC: 303-651-4248 Denver FSS: 720-873-2740 |
| --- | --- | --- |
|  | After initial coordination, and if Agency aircraft are available, request an AFRCC assigned search number, search radio frequency, and approval to conduct a route search, or a grid search (specific area(s)). If Agency aircraft are not available, request an aerial search by the responsible SAR agency. | Moffat County Sheriff: 824-4495 (#025 speed) Rio Blanco Sheriff: 675-8466(Rangely) (#034) 878-9620(Meeker) (#033) Eagle County: 970- 479-2201 Grand County: 970-725-3311 (#010) Jackson County: 970-723-4242 (#084) Summit County: 970-453-2232 |
|  | Continue coordination in-house and with other SAR agencies. Searches for missing aircraft may be short for local flights or may extend over several states and continue for several days for an aircraft missing on a cross country flight. The documentation (recording) of all actions and activities is mandatory. |  |

When the aircraft is located and has experienced a mishap, assure that all participating agencies are informed, then

proceed immediately into the recovery phase.  See Aircraft Accident procedures.

Note:  Aerial search missions are potentially hazardous.  Search aircraft must stay within their assigned and coordinated search area.  A common search radio frequency is mandatory.  The search aircraft making the ``find'' is further exposed to hazards due to excitement and desire to help.  Brief on (1) the danger of crashing at the crash site and (2) when the find is announced on the search frequency, all search aircraft clear the area unless specifically requested to participate in the

rescue phase.

###### MISSING AIRCRAFT

The following SHALL be notified.

This is normally done by the local aviation manager or designee.

| DATE/TIME NOTIFIED | ACTION | COMMERCIAL | HOME |
| --- | --- | --- | --- |

|  | Local Line Officers – John Husband (Little Snake FO) John Ruhs (Kremmling FO) Kent Walter (BLM White River FO) Mary Peterson (USFS) | 970-826-5089 970-724-3001 970-878-3802 307-745-2400 Laramie | 970-824-7410 970-724-9859 970-878-9828 307-721-4873 |
| --- | --- | --- | --- |

|  | Unit Aviation Officer – Cathy Hutton | 970-826-5032/5037 | 970-826-0694 |
| --- | --- | --- | --- |
|  | Regional /State/Area Aviation Safety Manager Kent Hamilton (BLM) (acting for USFS) Ivan Pupulidy (USFS) | 303-239-3809 303-275-5711 | 720-635-2994 (c) 970-241-8505 |

|  | Dispatch Center Manager - Cathy Hutton | 970-826-5032/5037 | 970-826-0694 |
| --- | --- | --- | --- |
|  | Geographic Coordination Center - RMACC | 303-445-4300 or (#015) |  |
|  | Local Personnel Clerk - Linda Berke (BLM) - Lila Coca (USFS) | 970-244-3060 307-745-2333 | 970-250-0744 (c) 307-745-7443 |
|  | Information Officers - Lynn Barclay (BLM) Diann Ritshard (USFS) | 970-826-5096 970-870-2187 | 970-824-6210 970-724-8926 |
| To start local Search and Rescue Operations contact: |
|  | Local Law Enforcement Officials. They will notify local search rescue unit if needed. |  |
|  | Eagle County Grand County | 970-479-2201 970-725-3311 (#010) |  |
|  | Jackson County Moffat County | 970-723-4242 (#084) 970-824-4495 (#025)(Admin) 970-824-6501 (Dispatch) |  |
|  | Rio Blanco County Summit County | 970-878-9620 (#033) 970-453-2232 |  |
| Fill out SAFECOM |

##### AIRCRAFT ACCIDENT

##### AWAY FROM CRASH/FIRE/RESCUE EQUIPPED AIRPORT

Aircraft accident notification may be the result of a search effort for a missing aircraft or may be an initial report from a

person or persons observing the mishap occurring, or locating a yet unreported missing aircraft.

The initial action, by the observer(s) of the mishap, should be reporting the mishap location.  The dispatch office or other agency designated office then becomes the action office for response, rescue, and notification.

The action office needs all the information immediately obtainable as to injured and/or deceased persons to request

adequate ambulance and life support equipment.  The absences of this information should not delay initiating life saving actions.  Early establishment of communications with the mishap site is critical.

Documentation of all actions, activities, contacts, conversations, aircraft and personnel dispositions, and times are mandatory.

| DATE/TIME NOTIFIED | Action | Telephone |
| --- | --- | --- |
|  | Notification received by designated action office. |  |
|  | Contact pre-designated rescue units: Agency (Helicopter, Rappellers, Smokejumpers, etc.) Cooperators (Military, Local Law Enforcement, etc.) |  |
|  | Air Ambulance Grand Junction - west side of Unit Flight for Life Denver - east side of Unit | 1-800-332-4923 1-800-332-3123 |
|  | Ground Ambulance (if applicable) | 911 |
|  | County Sheriff/State Police, etc. See Emergency Response Telephone list* | *Page 18 |
|  | Moffat County Coroner Routt County Coroner Rio Blanco County Coroner | 824-6133 879-0237 878-5730 |
|  | Notify agency staff for district, state, and/or area. See Aircraft Accident Notification Checklist** | **Page 8 |

|  | Notify FAA Flight Service Station to preclude search and/or rescue missions by others (example: ELT, if activated, will cause the National SAR Plan to be activated). | Denver ARTCC 303-651-4248 Denver FSS 720-873-2740 |
| --- | --- | --- |

|  | Arrange for security at the mishap site. See ``PREPARING FOR THE ARRIVAL OF THE INVESTIGATION TEAM.'' |  |
| --- | --- | --- |
|  | Obtain a FAR 91.137, temporary flight restriction, if needed. |  |
|  | Assign radio frequency as needed. |  |

Other agency follow-up actions may include deactivating the ELT

(most positive method is battery removal)

and notifying FSS of the deactivation.

AIRCRAFT ACCIDENT

AWAY FROM CRASH/FIRE/RESCUE EQUIPPED AIRPORT

Although one or two items in the sequence may be unknown at the time START THE ACTION.  Keep

an accurate written log and fill in the blanks as best you can.

As much as possible obtain the following information on the missing aircraft:

CAUTION: Do not announce over the radio the names of individuals involved in missing aircraft.

1. Name of pilot(s):

2. Name of passenger(s). How many?

3. Aircraft registration number ``N'' -

4. Type of aircraft -

5. Color of aircraft -

6. Type of mission -

7. Location of accident. Give latitude and longitude, if known. a. Locate on local agency map. b. Locate on aviation sectional chart. Plot radius from at least two VOR stations. Obtain latitude and longitude.

8. Date and time of accident.

9. Injuries or fatalities, if known. If information is given via radio, the names of deceased and/or seriously injured shall not be stated. Express need for coroner if there are fatalities.

10. Name, address, telephone number of person reporting accident.

11. Assistance at or on the way to accident site.

12. Nearest airport to accident site.

##### AIRCRAFT ACCIDENT NOTIFICATION CHECKLIST

Local aviation manager or designee shall notify the following as appropriate to their specific agency:   This is normally done by the local aviation manager or designee. (The local unit should modify this page to meet their needs).

| DATE/TIME NOTIFIED | ACTION | COMMERCIAL | HOME |
| --- | --- | --- | --- |
|  | Local aviation manager Cathy Hutton | 970-826-5032/5037 | 970-826-0694 |
|  | Local Line Manager/Officer John Husband (BLM Little Snake FO) John Ruhs (BLM Kremmling FO) Kent Walter (BLM White River FO) Mary Peterson (USFS) | 970-826-5089 970-724-3001 970-878-3802 307-745-2400 | 970-824-7410 970-724-9859 970-878-9828 307-721-4873 |
|  | Local County Sheriff's Office if they have not already been notified. Refer to the Emergency Response Telephone List | Page 18 |  |
|  | DOI/USDA-FS 24 hour Aircraft Accident Reporting Hot Line. | 1-888-464-7427 |  |
|  | Regional /State/Area Aviation Officer/Manager - Kent Hamilton (BLM) (Acting USFS) Ivan Pupulidy (USFS) | 303-239-3809 303-275-5711 | 720-635-2994 (c) 970-241-8505 |
|  | Geographic Area Coordination Center and/or Zone Coordination Center - RMACC | 303-445-4300 (#015 Speed Dial) |  |
|  | Local Personnel Officer Linda Berke (BLM) Lila Coca (USFS) | 970-244-3060 307-745-2333 | 970-250-0744 (c) 307-745-7443 |
|  | Local Public Information Officer - Lynn Barclay (BLM) Diann Ritshard USFS) | 970-826-5096 970-870-2187 | 970-824-6410 970-724-8926 |
|  | Ensure SAFECOM (FS) or Initial Report of Aircraft Mishap OAS-77 data form (DOI) have been completed. |  |  |

AIRCRAFT ACCIDENT

WITHIN CRASH/FIRE/RESCUE AIRPORT'S RESPONSE AREA

The planning for a mishap within the crash/fire/rescue (CFR) response area associated with an airport with established crash/fire/rescue procedures must include obtaining and posting the subject airport's (1) CFR plan, (2) emergency alarm/notification procedure and (3) the crash/rescue grid map of the response area.  Note:  The CFR plan and response

area map are available from Airport Manager.

The local CFR plan becomes primary in the initial rescue effort, with the agency being secondary.  Do not interfere with the established plan or, through lack of knowledge, duplicate efforts that lead to confusion and delays in life saving efforts.

Coordinate assumption of control of the mishap site (or removal of the mishap aircraft) with the CFR Agency, the FAA,

and the local law enforcement.

Documentation of all actions, activities, contacts, conversations, aircraft and personnel dispositions, and  times  is mandatory.

| Date/Time Notified | Action | Telephone |
| --- | --- | --- |
|  | Activate CFR plan immediately | See Emergency Response Telephone List p. 18 |
|  | Participate in CFR plan as requested by CFR plan agency |  |
|  | Notify agency staff for district, state, and/or area. See contacts and telephone numbers in previous section: Aircraft Accident - Away From Crash/Fire/Rescue Equipped Airport |  |
|  | Contact Regional /State/Area Aviation Manager/Officer or Aviation Safety Manager/Officer and complete SAFECOM (FS) or OAS-77 Form (DOI). |  |
|  | Arrange for security at the mishap site. See ``PREPARING FOR THE ARRIVAL OF THE INVESTIGATION TEAM.'' |  |

AIRCRAFT ACCIDENT

WITHIN CRASH/FIRE/RESCUE AIRPORT'S RESPONSE AREA

Although one or two items in the sequence may be unknown at the time START THE ACTION.  Keep an accurate written log and fill in the blanks as best you can.

As much as possible obtain the following information for the accident aircraft:

1. Activate Airfield/Helibase Crash Rescue.

2. Perform Rescue and Emergency Assistance.

3. Name of pilot(s):

4. Name of passenger(s). How many?

5. Aircraft registration number ``N'':

6. Type of aircraft.

7. Color of aircraft.

8. Type of mission.

9. Location of accident/name of airport. Give latitude and longitude, if known.

10. Date and time of accident.

11. Injuries or fatalities, if known. If information is given via radio, the names of deceased and/or seriously injured will not be stated. Express need for coroner if there are fatalities.

12. Name, address, telephone number of person reporting accident.

13. Assistance at or on way to accident site.

*Notify Local Dispatch and continue with notifications as presented in:

AIRCRAFT ACCIDENT - AWAY FROM CRASH/FIRE/RESCUE EQUIPPED AIRPORT

INITIAL ACTION CHECKLIST INSTRUCTIONS TO RESCUE PERSONNEL

## ASSESS THE RISK FIRE, FUEL, HAZARDOUS MATERIALS   ASSESS THE RISK  FIRE, FUEL, HAZARDOUS MATERIALS

1.	Assist Survivors:  Administer first aid to the injured and transport as soon as possible.

2.	If there is any danger of a fire, move survivors a safe distance away.  Establish a ``NO SMOKING'' rule; fire and explosion are a real danger with residual fuel and hot metals.

3.  	Conduct thorough search of the accident site and surrounding area for additional survivors.

4.  	Establish communications with Unit Dispatcher and/or rescue personnel and with the Accident Scene Officer-in-Charge (see ``Preparing for the Arrival of the Investigation Team'').  Inform appropriate personnel (dispatcher/law enforcement officer) if there is a need for a coroner.  The coroner will give instructions for removal and transportation of bodies.  Notify appropriate personnel (dispatcher/law enforcement officer) of best method of transporting injured personnel:

a. Ambulance helicopter

b. Ambulance fixed-wing

c. Ground ambulance

5. 	Secure and preserve the accident site:

a. 	Flag or rope off the accident site area (Note: Accident site may extend a significant distance from the

aircraft).  Do not disturb accident site except for life-saving purposes (e.g. extraction of personnel).

- Request law enforcement (agency and/or local).  Allow only authorized personnel on the accident site. Keep bystanders and unauthorized personnel away from the accident site until arrival of law enforcement.  Aircraft may be released only by the Contracting Officer.  After an accident, the aircraft is    no longer the vendor's property until released by the CO.

c.	If no road access or emergency medical service (EMS) helicopter has been requested, prepare helispot.

Assign most-qualified personnel to manage.

6.  Identify all witnesses:

a. Name

b. Address

c. Telephone Number

d. Record on tape or have witness write down preliminary statement.

7.  Keep a record of all the actions completed and give to the accident investigation team.

PREPARING FOR THE ARRIVAL OF THE INVESTIGATION TEAM

This is a checklist of some tasks, which both the Line Manager and Aviation Manager can use to take charge of the accident scene and prepare for the arrival of a trained aircraft accident investigator and/or the aircraft accident investigation team.  Some items may not be applicable and others may need to be added, depending on the circumstances of the accident.  This list was developed with the objective of providing a place to start during upsetting times.

- General

The local Line Manager should establish an Officer-in-Charge of Search/Rescue.  The first agency employee to arrive at the scene of the accident will be responsible for crash site protection until relieved by the Accident Scene Officer-in-Charge, or by the appointed accident investigation team.  Accident scene protection by the Line Manager can last from a few hours to several days, depending upon location, accessibility, etc.  The time will depend on which level of the organization will take jurisdiction, what intermediate actions are taken and how long it will take the investigation team to travel to the site, assemble, organize, and take charge.

- Off-Scene Responsibilities

The Officer-in-Charge will ensure the following off-scene tasks are accomplished:

1.  Procedures in this Aircraft Crash, Search, and Rescue Guide are followed; emergency notifications made

promptly.

2.  Determine accident scene land ownership.  If the accident site is determined to be on Private or State Lands, ensure that notification is made to the appropriate parties.

3.  Inform receptionists and others who may answer the telephone to pay particular attention to anyone calling in who may have witness information.  The investigation team will want to contact those persons, so they will

need names and telephone numbers for later contact.

4.   Prepare a list of names, telephone numbers, addresses, etc., of all known witnesses at or near the  accident scene.

5.   Obtain all available weather data for the area.  Order additional weather information to be taken at weather

stations in the area, and be prepared to do it again 24 hours later.  The information may be needed to compare with weather readings at the accident scene to estimate the weather at the time and place of the accident.

6.   Determine when and where the aircraft was last fueled, and request the supplier to take fuel samples for the agency to pick up later.  It is best if the Officer-in-Charge can do the fuel sample at the last fueling site; but it is recognized that this is no always possible.

7.   Obtain the following names and telephone numbers:

a. The sheriff or other local law enforcement officer having jurisdiction.

b. The coroner or other person having jurisdiction over the removal of the remains.

c. The attending medical doctor for those injured in the accident.

d. The landowner if the accident occurred off Federally owned lands.

e. The names and telephone numbers of any reporters who have requested information for media

dissemination.  The chief investigator or Agency PIO will be in touch with them, when information

becomes available.

PREPARING FOR THE ARRIVAL OF THE INVESTIGATION TEAM

8.  Arrange transportation for the use of the investigation team.  Two vehicles will probably be needed and one

person who is familiar with the area-hospital, sheriff's office, witness addresses, etc.  A helicopter and/or

airplane may be needed for transportation of the team to remote sites.

9.   Arrange lodging for the team at a city/town nearest the accident site.

10.  Prepare for a brief entrance conference with the chief investigator upon his arrival.  The local Line Manager should make available all personnel involved in the flight (Aviation Manager, Dispatcher, etc.)

11.  Obtain five topographic and agency maps of the area.  Aerial photographs, if available, plus any other maps the unit believes will be helpful to the investigation team, should be included.

12.  If the aircraft was under contract to the agency, secure a copy of the contract for the investigation team.

13.  Obtain agency radio logs, tapes, flight request/schedule, weather observations and forecasts, etc., that may contain information (no information can also be evidence) relating to the accident.

14.  Determine whom the Line Manager wants to designate as the unit's primary contact with the chief  investigator.

15.  Establish a work area with desk, telephone, and computer station for use by the chief investigator.

C.   On-Scene Responsibilities

The Officer-in-Charge will ensure the following on-scene tasks are accomplished.

1.  Deactivate (disable) the emergency location transmitter (ELT).  (Most positive method is battery removal).

2.  Prevent unauthorized people from conducting activities that will destroy important information.  Ground impact points should be preserved; that is, people should not be walking around to satisfy their curiosity.  They may damage evidence.

3.  Ensure that personnel involved in the search and rescue do not broadcast the names of aircraft occupants or state the extent of injuries over the radio system.

4.  Personnel should be advised that the wreckage is hazardous.  Fuel can burn; tires can explode; gases and

metals can be ingested by the body; bacteria can be present; corrosive liquids may be exposed; liquid and solid poisons may be present; chemical reactions may have occurred, especially if there has been a fire; personal baggage and equipment contain unknown items; etc.  The Officer-in-Charge should stay away from the wreckage and keep others away from it until a trained aircraft accident investigator arrives. Personal risk should only be taken to assist evacuation of the injured.  The removal of bodies falls within the Coroner's

(local/State/county) authority.

5.  Prepare written notes on all activities at the accident scene.  Each recording should include the date and time of the activity and observation.  Ensure an accurate recording will be made by someone until the wreckage is removed.  Examples include:

a. The time the agency Officer-in-Charge arrived at the scene.

b. Other personnel who were or may have been at the accident location (date/time/location relative 	to the crash site) before the arrival of the Officer-in-Charge.

c. Weather observations and any odors (such as fuel) noticed upon arrival.

d. Any wreckage moved or removed and by whom.

e. First aid and medical assistance rendered to the injured.

f. Removal of fatally injured persons necessitates the recording of: (see next page)

(1)  Which body came from which seat, or where it was found.

(2)  Seat belt usage (or lack thereof).

(3)  A description of type and color of clothing.

(4)  A witnessed statement (inventory of personal effects removed, such as counting cash in wallet, listing all identification cards, match books, loose pocket change, keys, pocket notebooks, pens, personal protective equipment worn or found).

(5)  Names of all persons visiting the accident scene after arrival of the Officer-in-Charge.

(6)  Any other information that might help the investigation team.

6.  Take photographs, if possible, before removing remains or disturbing wreckage.  This should be foregone if

there are injured that need to be evacuated.  In that case a written recording and/or photographs taken after the fact will suffice.   Preserving life is the number one priority.

7.  Flag or rope off the accident scene to prevent unauthorized access. Colored flagging is preferred, to allow for later pictures taken from the air by the investigation team.

8.  Accept all written narrative witness statements, place them in an envelope, and transmit them to a central point for collection by the investigation team or by the first trained investigator that arrives.  To the extent possible, do not allow anyone to verbally question the witness.  Questions by an untrained person can contaminate (modify and/or change) the information the witness will provide.  Encourage written statements made by each person; attempt to separate all witnesses.

9.  Take all other prudent actions to:

a. Preserve life

b. Protect people at the scene

c. Protect and preserve information

REQUEST INFORMATION - HELICOPTER AMBULANCE

A.  Injury Information:

1.	Total personnel involved in mishap ___________________________________________________________

2.   	Time of mishap _________________________________________________________________________

3.	Type or extent of injuries (vitals, other medical personnel on scene) ________________________________

_____________________________________________________________________________________

_____________________________________________________________________________________

_____________________________________________________________________________________

B.  Mishap Site Information:

1.  Unit/Agency ____________________________________________________________________________

2.  Contact telephone number__________________________________________________________________

3.  Radio frequency to contact unit/agency:  VHF-AM_________ VHF-FM__________

4.  Location of mishap:

a. Township_______Range_______Section______1/4 Section_____________

b. Latitude________________________ Longitude____________________________

c._______Nautical miles at___________Degrees from_____________________________________VOR

d. Prominent landmark:  Distance______________________    Direction________________________

5.  Site Contact ____________________________________________________________________________

Radio frequency at mishap site:

Primary:  VHF-AM___________________________ VHF-FM___________________________

Secondary:  VHF-AM_________________________ VHF-FM___________________________

6.  Other known aircraft in the area (call signs) ____________________________________________________

Air-to-Air Frequency:

Primary:  VHF-AM__________________________ VHF-FM____________________________

Secondary:  VHF-AM________________________VHF-FM_____________________________

7.  Special information, flight hazards, etc. _______________________________________________________

__ ___ _____________________________________________________________________________________

_________________________________________________________________________________________

8.  Landing site(s) and conditions (is it completed or when will it be completed):

_________________________________________________________________________________________

_________________________________________________________________________________________

9.  Proximity of landing site to mishap site  ______________________________________________________

________________________________________________________________________________________

10.  Nearest available AV Gas/Jet A fuel	________________________________________________________

11.  Conditions at the mishap site:

Wind direction____________________________	Wind velocity__________________________

Ceiling and visibility ________________________           Obstructions to visibility _________________

__________________________________________________________________________________

Degrees (F or C) ________Elevation ___________Sunrise ___________ Sunset _________________

Description of Terrain_________________________________________________________________

__________________________________________________________________________________

__________________________________________________________________________________

Note:  EMS helicopters do not usually carry extrication equipment nor are the EMS personnel always trained in

these procedures:  Ensure that if is capability is needed, it is immediately ordered from a locally known source

(the local sheriff is a logical contact point).

EMERGENCY RESPONSE TELEPHONE LIST

|  | COMMERCIAL PHONE | 24 HOUR PHONE |
| --- | --- | --- |
| LOCAL LAW ENFORCEMENT: Craig Police Meeker Police Rangely Police Colorado State Patrol | 970-824-8111 970-878-5555 970-675-8466 (#034) 970-824-6501 (#032) |  |
| LOCAL LAW ENFORCEMENT: Dinosaur Police Hayden Police Steamboat Police | 970-374-2466 970-276-3232 970-879-1144 |  |
| COUNTY/STATE LAW ENFORCEMENT: Eagle County Grand County Jackson County | 970-328-8564 970-725-3311 (#010) 970-723-4242 (#084) |  |

| COUNY/STATE LAW ENFORCEMENT: Moffat County Rio Blanco County Summit County Routt County | 970-824-6501 (#025) 970-878-9620 (#033) 970-453-2232 970-879-1110 (#035) |  |
| --- | --- | --- |

| HOSPITAL: Memorial (Craig) | 970-824-9411 | same |
| --- | --- | --- |
| HOSPITAL: Pioneers (Meeker) | 970-878-5047 | same |
| BURN CENTER: Children's - Denver Salt Lake | 303-861-8888 801-581-2700 | same same |
| POISON CENTER: | 1-800-332-3073 |  |
| GROUND AMBULANCE SERVICE: | 911 |  |
| LOCAL UTILITY COMPANIES: GAS: ATMOS Gas ELECTRIC: Yampa Valley Electric | 1-888-442-1313 970-824-6593 | 1-800-662-6185 (emergency) 970-879-1160 |
| EMS HELICOPTER: |  |  |
| EMS HELICOPTER: |  |  |
| EMS HELICOPTER: |  |  |
| MILITARY HELICOPTER (EMS): |  |  |
| FIXED WING AMBULANCE SERVICE: |  |  |

FOREST SERVICE

AVIATION RELATED ACCIDENT/INCIDENT AGENCY CONTACT LIST

| FOREST CONTACT | NAME | OFFICE/CELL/PAGER | HOME PHONE |
| --- | --- | --- | --- |
| FOREST SUPERVISOR | Mary Peterson | 307-745-2400 | 307-721-4873 |

| FOREST AVIATION OFFICER | Cathy Hutton | 970-826-5032/5037 | 970-824-0694 |
| --- | --- | --- | --- |
| FIRE MANAGEMENT OFFICER | Cliff Hutton (acting) | 970-826-5030/C:326-6777 | 970-826-0694 |
| PERSONNEL OFFICER | Lila Coca | 307-745-2333 |  |
| ADMINISTRATIVE OFFICER | Susan Kay | 307-745-2406 | 307-745-5222 |
| PUBLIC INFORMATION OFFICER | Diann Ritshard | 970-870-2250 | 970-724-8926 |
| LAW ENFORCEMENT OFFICER | Dan Nielson(Yampa) Curt Orde (Laramie) | 970-638-4516 307-745-2442 C: 307-377-9287 | 970-870-5957 307-721-6500 |
| RENEWABLE RESOURCE STAFF | Rick Rhine | 307-745-2410 | 307-742-6523 |

| USFS REGIONAL Office | NAME | OFFICE/CELL/PAGER NUMBER | HOME PHONE |
| --- | --- | --- | --- |
| REGIONAL AVIATION SAFETY MANAGER | IVAN PUPULIDY | OFF (303)275-5711 CELL (729)480-0495 | 303-973-4041 |
| REGIONAL AVIATION OFFICER | TOM LANDON | OFF.(303) 275-5740 CELL(303)886-2124 | (303)670-4457 |
| REGIONAL DIRECTOR, STATE & PRIVATE | MARK BOCHE | OFF(303) 275-5736 CELL(303)570-8971 | (303) 989-3203 |

| DEPUTY DIRECTOR, STATE & PRIVATE | LINDON WIEBE | OFF(303) 275-5750 CELL(303)570-8515 | (303) 904-6826 |
| --- | --- | --- | --- |

| REGIONAL FORESTER | RICK CABLES | OFF(303)275-5450 |  |
| --- | --- | --- | --- |
| DEPUTY REGIONAL FORESTER, S&PF | RICHARD STEM | OFF(303) 275-5452 |  |
| REGION HEALTH AND SAFETY MANAGER | CARLOS PINTOS | OFF(303) 275-5312 |  |
| REGIONAL DIRECTOR, HUMAN RESOURCES | Vacant | OFF(303) 275-5305 |  |
| REGIONAL AVIATION CONTRACTING OFFICER | DIANA PATERA | OFF(303) 275-5288 |  |

#### FAA TELEPHONE NUMBERS  FAA TELEPHONE NUMBERS

| FAA OFFICE | PHONE NUMBER |
| --- | --- |
| LOCAL TOWER |  |
| FLIGHT SERVICE STATION (FSS); | 1-800-843-5619 |
| DENVER FSS (COLORADO) | 303-799-7000 |
| CASPER FSS (WYOMING) | 307-235-1555 |
| HURON FSS (SOUTH DAKOTA) | 605-352-3806 |
| COLUMBUS FSS (NEBRASKA) | 402-564-3293 |
| WICHITA (KANSAS) | 316-942-4131 |

BUREAU OF INDIAN AFFAIRS

AVIATION RELATED ACCIDENT/INCIDENT CONTACT LIST

| BUREAU OF INDIAN AFFAIRS | NAME | OFFICE/CELL/PAGER NUMBER | HOME |
| --- | --- | --- | --- |
| Regional Aviation Manager (Southwest) | Denny Bridges | (O) (505) 842-3869 (C) (505) 220-0035 |  |
| Regional Aviation Manager (Northwest) | Joel Kerley | (O) (406) 329-4720 (C) (406)239-0643 |  |
| Regional Aviation Manager | Mike Amicarella | (O) (303) 387-5371 (C) (303) 888-1505 | 970-586-3227 |
| National Aviation Manager | Mike Amicarella (acting) | (O) (208) 387-5371 (C) (208) 888-1505 | 970-586-3227 |
| BIA NIFC Director | Lyle Carlile | (O) (208) 387-5697 (C) (208) 869-7803 |  |
| Area Office Aviation Manager |  |  |  |
| Area Fire Management Officer |  |  |  |
| BIA Area Director |  |  |  |
| Agency Aviation Manager |  |  |  |
| Agency Fire Management Officer |  |  |  |
| Agency Superintendent |  |  |  |

COLORADO BUREAU OF LAND MANAGEMENT

AVIATION RELATED ACCIDENT/INCIDENT AGENCY CONTACT LIST

| BUREAU OF LAND MANAGEMENT, CO | NAME | OFFICE/CELL/PAGER NUMBER | HOME PHONE |
| --- | --- | --- | --- |
| STATE AVIATION MANAGER | KENT HAMILTON | (303) 239-3809 (303)239-3811 FAX CELL (720)635-2994 |  |
| STATE FIRE MANAGEMENT OFFICER | BILL WALLACE | (O) (303) 239-3689 CELL (303)881-2441 | (303)425-7284 |
| STATE EXTERNAL AFFAIRS, PUBLIC INFORMATION OFFICER | BARB PERKINS | (303)239-3668 CELL (720)480-2795 | (303)670-1650 |
| STATE SAFETY MANAGER | JOHN DEVORE | (303)239-3650 CELL (970)412-0825 | (970)461-2928 |
| STATE SPECIAL AGENT (LEO) | JOHN SILENCE | (O)(303) 239-3803 (C)(303) 550-1232 (P)(888) 787-6023 | (303)986-1833 |
| STATE PERSONNEL OFFICER, HUMAN RESOURCES | MELISSA DUKES | (303) 239-3920 | (303)430-7876 |
| STATE DIRECTOR | RON WENKER | (303) 239-3700 CELL: (720) 560-2985 | (303)-526-0184 |
| ASSOCIATE STATE DIRECTOR | DOUG KOZA | (303) 239-3702 CELL(303)618-1177 | (303)471-8413 |
| DEPUTY STATE DIRECTOR, SUPPORT SERVICES | LINDA ANANIA | (303) 239-3745 CELL: (970) 406-0440 | (303) 456-5871 |
| NATL. AVIATION GROUP MANAGER | DAVE DASH | (208)387-5448 CELL(208) 863-4366 | (208) 365-0903 |
| NATL. AVIATION SAFETY MANAGER | LARRY MAHAFFEY | (208)387-5160 CELL(208)841-1042 | (208)672-8126 |

###### DO NOT RELEASE HOME TELEPHONE NUMBERS

###### TO THE PUBLIC OR THE MEDIA

CALL THE CELLULAR TELEPHONE NUMBER

BEFORE CALLING THE HOME TELEPHONE NUMBER

WYOMING BLM TELEPHONE CONTACT LIST

BUREAU OF LAND MANAGEMENT

AVIATION RELATED ACCIDENT/INCIDENT AGENCY CONTACT LIST

| BUREAU OF LAND MANAGEMENT,WY | NAME | OFFICE/CELL/PAGER NUMBER | HOME PHONE |
| --- | --- | --- | --- |
| STATE AVIATION MANAGER | KURT KLEINER | (307) 775-6237 (307) 630-0070 | (307) 632-5756 |
| STATE FIRE MANAGEMENT OFFICER | JOHN GLENN | (307) 775-6234 (307) 631-9347 |  |
| STATE PUBLIC INFORMATION OFFICER | STEVE HALL | (307) 775-6015 |  |
| STATE SAFETY OFFICER | SHORTY LOWDERMILK | (307) 775-6269 (307) 631-9502 |  |
| STATE SPECIAL AGENT (LEO) | MIKE MILLER | (307) 775-6266 (307) 421-1900 |  |
| STATE PERSONNEL OFFICER | DERI YOUNG | (307) 775-6036 (307) 631-1670 |  |
| STATE DIRECTOR | BOB BENNETT | (307) 775-6001 (307) 631-2350 |  |
| ASSOCIATE STATE DIRECTOR | ALLEN KESTERKE | (307) 775-6001 (307) 631-8911 |  |
| DEPUTY STATE DIRECTOR | DON SIMPSON | (307) 775-6113 (307) 631-8910 |  |
| BLM ROCKY MTN. AREA COORDINATOR | JOHN GLENN | (303) 775-6234 | (307) 635-3104 |

NATIONAL PARK SERVICE TELEPHONE CONTACT LIST

AVIATION RELATED ACCIDENT/INCIDENT AGENCY CONTACT LIST

| TITLE | NAME | OFFICE/CELL/PAGER NUMBER | HOME PHONE |
| --- | --- | --- | --- |
| NATIONAL AVIATION PROGRAM AND SAFETY MANAGER | BILL SPRUILL | (202) 208-6258 |  |
| INTERMOUNTAIN REGIONAL AVIATION MANAGER | LEN DENS | (303) 969-2449 |  |
| MIDWEST REGIONAL AVIATION MANAGER | DOUG ALEXANDER | (402) 661-1754 (402) 630-0685 |  |
| OAS AVIATION SAFETY MANAGER | BOB GALLOWAY | (208) 433-5071 |  |

|  |  | DINOSAUR NATIONAL PARK TELEPHONE NUMBERS |  |
| --- | --- | --- | --- |

| TITLE | NAME | OFFICE/CELL/PAGER NUMBER | HOME PHONE |
| --- | --- | --- | --- |
| ACTING PARK SUPERINTENDENT | MARY RISSER | 970-374-3001 | 970-374-2266 |
| PARK AVIATION OFFICER | CATHY HUTTON | 970-826-5032/5037 | 970-826-0694 |
| PARK FMO | MARK ROSENTHAL | 970-374-3024 sat:254-381-5343 c: 970-629-0191 | 970-374-2752 |
| PARK AFMO | MATT WOOD | 970-374-3011 sat:251-381-5339 c: 970-629-0192 |  |

FISH AND WILDLIFE SERVICE TELEPHONE CONTACT LIST

AVIATION RELATED ACCIDENT/INCIDENT AGENCY CONTACT LIST

| TITLE | NAME | OFFICE/CELL/PAGER NUMBER | HOME PHONE |
| --- | --- | --- | --- |
| NATIONAL AVIATION MANAGER | BILL BUTLER | 505-248-6508 c: 571-239-9599 fax: 505-248-6673 |  |
| REGIONAL AVIATION MANAGER | KEVIN FOX | 701-355-8531 |  |
| AVIATION OPERATIONS SAFETY SPECIALIST | MIKE JEFFERIES | 208-387-5864 c: 208-850-3022 fax: 208-387-5735 |  |

BROWNS PARK NATIONAL WILDLIFE REFUGE

| TITLE | NAME | OFFICE/CELL/PAGER NUMBER | HOME PHONE |
| --- | --- | --- | --- |
| REFUGE MANAGER/LEO | LEE ALBRIGHT | 970-365-3613 ext: 203 c: 970-269-7077 | 970-365-3002 |
| REFUGE AVIATION OFFICER | CATHY HUTTON | 970-826-5032/5037 | 970-826-0694 |
| ZONE FMO | KEN KERR | 303-445-4369 c:303-886-7830 | 303-568-3055 |
| ZONE AFMO | JOE FLORES | 970-365-3613 ext: 204 c: 326-5084 s: 254-381-8784 | 970-365-3777 |